# Text boxes

Raysun H-168 & HID-2

Powerful Rechargeable Searchlight

Security Defense & Tactical Devices - 06

P.09

Raysun HID-2

- Hand-held/shoulder-carry, illuminating distance up to 1.200 meters.

- Reinforced aeronautic aluminum alloy casing, water-proof, suit for sea or coast activities, rescue & fire control…etc.

- Can be attached to weapon with Picatinny rail mount easily.

- 4 optional filters: Red, Blue, UV & IR.

- Comes with high intensity carrying case, water-proof as well as vibration protection.

Raysun H-168

Optional filters:

- Hand-held / shoulder-carry, illuminating distance up to around 800 meters.

- Both indoor AC power or vehicle DC power recharge, easy for operation & carry.

- Can be fully Immersed into water, especially for sea or coast activities.

- Low power alert function (to 10 minutes).

Red

IR

UV

Blue

( Specifications:

| Model | H-168 (X) | H-168 (H) | HID-2 |
| --- | --- | --- | --- |
| Outer construction material | ABS | Reinforced aeronautic aluminum alloy casing, Military standard TYPE II hard anodizing processing |
| Dimensions | 270(L) x 170(W) x 180 (H) mm | Diameter: Ø120, 225(L) mm |
| Weight | Below 2500g | Below 2800g |
| Power switch | 3 light mode: ON／OFF／Manual flash | 2 light mode: ON／OFF |
| Lamp | 55W/100W Xenon | 35W HID | 35W HID |
| Illuminating intensity | Above 2,500/ 3500Lux at 10M distance of parallel light axis | Above 3,500Lux at 10M distance of parallel light axis Max. output luminance: 3,200 lumens |
| Power supply | w/rechargeable Ni-MH battery, continuously light-up for over 80 minutes | w/rechargeable Lithium battery, continuously light-up for over 120 minutes | w/rechargeable Lithium battery, continuously light up for 90 minutes above |
| Protection level | Immersed to water, IP-66 | IP-56 |
| Optional filters | None | Red: 590~640nm; rescue/signal/ multimedia or outdoor photography blue: 450nm; signal UV: 365nm; to reveal UV reactive materials, such as fingerprints, bloodstain, footprint, banknotes, gems, minerals, bacteria…etc. IR: 800nm; invisible light |

with red filter

with blue filter

4

1

2

4

1

with UV filter

3

3

2

( Raysun HID-2 standard package:

- HID-2 powerful rechargeable searchlight

- AC100~240V charger

- Nylon adjustable shoulder carry strap

- Hard high intensity carrying case

( Raysun H-168 standard package:

- H-168 rechargeable water-proof searchlight

- AC100~240V charger

- Vehicle DC charger

- Nylon adjustable shoulder carry strap

with IR filter

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.