# Text boxes

Raysun ARG-3

Multi-functional Soft-gun

Security Defense & Tactical Devices - 04

P.07

Operate with optional “Front/rear air intake bottle“ & “Hopper“

Long/short barrel changeable

( Key features:

- Semi-auto shooting mechanism, powerful non-lethal weapon, especially suit for Anti-riot purpose.

- Magazine for loading various balls: Pepper ball, Rubber ball and Color ball, Training ball ...etc.

- CO2 condensed gas cylinder as its propellant power, easy for operation and safe for storage.

- Features a pressure meter for measuring the remaining gas volume.

- Interchangeable long & short barrels.

- Endurable aluminum alloy material construction.

- This non-lethal weapon had been effectively used to anti-riot in the Seattle (US) riot event, WTO (HK) publics event, US Coast Guard, prison management, immigration office…etc.

- Attached Picatinny rail for coupling with any standard accessories easily (like tactical light, laser sight…etc.)

- Optional coupling with our TPL-5/-6/-10 powerful tactical flashlight for multi-applications.

- Optional “Front/rear air intake bottle” & “Hopper”.

( Specifications:

| Model | ARG-3 |
| --- | --- |
| Construction material | T6 aluminum alloy, anti-slip and vibration proof rubber on grip |
| Dimension | 25cm (L) x 17cm (H) (without accessories) |
| Weight | Below 1 Kg (without accessories) |
| Kinetic energy | 17 joules @ muzzle / 10 joules (max.) @ 20M from muzzle |
| projectile power | *Front CO2 condensed gas cylinder, 12g/24 shoots *Rear CO2 condensed gas cylinder, 70g/60~80 shoots. Can refuel CO2 gas. |
| Shooting mode | Semi-auto |
| Barrel length | Short barrel (5cm) | Long barrel (27cm) |
| Speed measurement (@position from muzzle) | approx. 55m/s @5m approx. 47m/s @10m approx. 42m/s @15m approx. 33m/s @20m | approx. 75m/s @5m approx. 65m/s @10m approx. 63m/s @15m approx. 48m/s @20m |
| Temperature | -10°C ~ 55°C |
| Warranty | One year |

5

3

6

4

3

1

2b

2c

2a

( Options:

- 1913 Picatinny rail mount

- TPL-5 or TPL-10 extra high brightness tactical flashlight

- Laser sight

- Pepper ball/Rubber ball/Color ball/ Training ball

- CO2 condensed gas

cylinder

- Front/rear air intake bottle

(Can refuel CO2 gas)

- Hopper (can put around

150 pcs balls)

Color ball ball

Rubber ball

Training ball

( Standard package:

- ARG-3 main body x1

- Magazine of 9 balls capacity *1

- CO2 condensed gas cylinder (12g) *3

- Interchangeable long/short barrels *1/each

- Rubber/color/training balls x20/each

*Appearance and color may different with following pictures.

- Assembling tools kit *1

- Shoulder strap *1

ARG-3 + TPL-5 or -10

Please use this device by local law regulation; we have not responsibility if any lawbreaking usage or behavior happened.

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.