# Text boxes

Raysun STC-J10 series

Eyeglasses-type Hidden Cameras

Special surveillance Devices –11-1

STC-J10B

STC-J10A

- Professional sport sunglasses feature, can even cover on your original diopter eyeglasses if needed.

- Use anti UV400 Polarized light explosion- proof safety lenses, glare/reflection proof.

- Auto secure photographic color-change lenses.

- Perfect covert camera device, co-work with DVR or wireless transmitter for remote monitoring/recording.

- 具頭戴式、胸掛式兩款

- Stylish feature with metallic frame.

- User can replace suitable diopter lenses by themselves if necessary.

- NTSC/PAL systems switchable.

- Indoor/outdoor audio modes switchable.

- Perfect covert camera device, co-work with DVR or wireless transmitter for remote monitoring/recording.

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

P.14

( Options:

- Digital A/V recorder: DVR-2/DVR-2 plus/DVR-3

- Wireless transmitter

- Wireless receiver

- WRD-3 wrist-wear wireless A/V receiver/recorder

STC-J10B co-work

with DVR

記錄器工作架構

( Specifications:

| Model | STC-J10A | STC-J10B |
| --- | --- | --- |
| Image sensor | 1/4" CMOS Sensor | 1/18" CMOS Sensor |
| Min. illumination | 0.1 Lux/F1.2 | 0.1 Lux/F1.2 |
| Lens F/No | 3.4 | 2.8 |
| Lens focus | 3.1mm | 0.99 mm |
| Field of view | 78° ± 2° | 60° ± 2° |
| Video resolution | 400 TV Line | 480 TV Line |
| Digital photo resolution | 640x480 | NTSC: 720x525 (max.); 640x480 (standard) |
|  |  | PAL: 720x625 (max.); 640x480 (standard) |
| Electronic shutter | 1/60(N); 1/50(P)~1/10,000 |
| Video output | 1.0 Vp-p |
| Microphone | yes |
| Power Voltage | DC 5V |
| Power Current | 110 mA |
| Video system switchable | NTSC/PAL |
| Audio mode switchable | Indoor/outdoor mode |
| Dimensions | 50x55x160mm | 25x35x135mm |
| Weight | around 60 g | around 20 g |

STC-J10B

DVR

STC-J10A

Receiver

Transmitter

WRD-3 wrist-wear wireless A/V Receiver/Recorder

or

TX

Monitor

or

RX