# Text boxes

HTC-J16 series

Head/Ear-wear type Hidden cameras

Special surveillance Devices –11-2

HTC-J16B

HTC-J16A

- Come with head/helmet-wear fixture & vehicle multi-functional fix gadget for military/police surveillance mission.

- Tie-type remote controller and anti neck reined design for easy & safe operation.

- IR sensible camera, day/night auto change, low illumination with 500TVL high resolution.

- Can optional co-work with visible or invisible auxiliary light.

- No need external battery while co-work with our DVR devices.

LED light/right-side

Camera/left-side

- No influence to wear any kind of helmet.

- Camera flat-puts on the face-side comfortably, viewing direction flexibly adjustable.

- Perfect covert camera device, co-work with DVR or wireless transmitter for remote monitoring/ recording.

( Specifications:

| Model | HTC-J16A | HTC-J16B |
| --- | --- | --- |
| Video system | NTSC/PAL |
| Image sensor | 1/4” interline CCD | 1/3” interline CCD |
| Min. illumination | 0.5Lux/F2.0 | 0.2Lux/F2.0 |
| Lens | 4.3mm/78° | 6mm/51° |
| Video resolution | 450 TV line | 550 TV line |
| Pixels | 768x492 | 811x508 |
| Electronic shutter | 1/60~1/10,000 | 1/60~1/120,000 |
| Audio output | 1.0 Vp-p |
| Microphone | yes |
| Power voltage | 5V+/-0.5V |
| Power current | 220 mA |
| Dimensions (camera only) | 29x25x29mm | ψ20x50.5mm |
| Weight | around 40g | around 39g |

HTC-J16A

HTC-J16B

Transmitter

or

TX

DVR

( Options:

- Digital A/V recorder:DVR-2/DVR-2 plus/DVR-3

- Wireless A/V transmitter

- Wireless A/V receiver

- WRD-3 wrist-wear wireless A/V receiver/recorde

- Visible or invisible (HTC-16B only) auxiliary light

RX

or

Receiver

WRD-3 wrist-wear wireless A/V Receiver/Recorder

Monitor

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

P.15