# Text boxes

Special surveillance Devices -11-3

ETC-J14/BTC-J20

Earphone & Button type Hidden Cameras

BTC-J20

ETC-J14

Various types button/screw accessories changeable

BTC-J20 Button type

ETC-J14 Earphone type

( Specifications:

| Model | ETC-J14 | BTC-J20 |
| --- | --- | --- |
| Video system | NTSC/PAL |
| Image sensor | 1/4” Color CMOS | 1/3” interline CCD |
| Min. illumination | 3 Lux | 0.2Lux |
| Lens | 3.59mm/F2.0 | 4.3mm/F1.8 |
| Field of view | 66.5° |  |
| Video resolution | 480 TV line | 550 TV line |
| Pixels | 640 x 480 | 768x492 |
| Video output | 2Vp-p(MAX) 10KHz ohms Impedance |
| Microphone | yse |
| Power voltage | 5V+/-0.5V |
| Power current | 130 mA | 60 mA |
| Dimensions | 23(L)X26(W)X18(H) | 28(L)X24(W)X18(H) |
| Weight | around 25 g | around 22 g |

( Features:

- ETC-J14 covert as a earphone feature, suit for side monitoring/ recording.

- Co-work with portable DVR easily

- BTC-J20 covert as a cloth button for perfect spy surveillance.

- Attach various button/screw accessories for replacement

DVR

Receiver

Transmitter

WRD-3 wrist-wear wireless A/V Receiver/Recorder

Monitor

or

or

TX

RX

RX

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

( Options:

- Digital A/V recorder: DVR-2/DVR-2 plus/DVR-3

- Wireless transmitter

- Wireless receiver

- WRD-3 wrist-wear wireless A/V receiver/recorder

P.16