# Text boxes

Raysun

Various wireless A/V Transmitters

Special surveillance Devices -13-1

JT-1205C8 (0.5W)

JT-1240C4 (4W)

JT-1210C8 (1W)

( JT-1240C4 (4W)

- 4W high power wireless A/V transmitter, high efficient PLL power transform & power-saving design, current consumption is only 1A/12VDC.

- Works with either rechargeable or vehicle battery, suit for A/V transmission in rescue, surveillance and any difficult environments mission.

- Large cooling blade & forced cooling system for long time transmitting.

- 2 A/V input, can co-work with camcorder, CCD camera and various hidden cameras via a Ø2.5mm/DC5V connector.

- Transmission distance: 500M above/standard antenna; 1,000M above/10dB directional antenna.

( JT-1205C8 (0.5W)/ JT-1210C8 (1W)

- Small size, light weight, built-in rechargeable battery.

- Battery running time: JT-1205C8 to 90 minutes above; JT-1210C8 to 50 minutes above.

- JT-1210C8 with 0.5W/1W switchable output power.

- 8 channels.

- Low power & signal interrupted alert by LED indicator.

- A Ø2.5mm/DC5V video input and 5V/DC output to supply camera battery use.

( Standard package: 4W transmitter/receiver/power adapter

10dBdirectional antenna

Example (2)

Example (1)

Co-work with CCD, camcorder & various hidden cameras

JT-1210C8

Hidden camera

( Specifications:

| Model | JT-1205C8 | JT-1210C8 | JT-1240C4 |
| --- | --- | --- | --- |
| Frequency range | 1200MHz | 1200MHz | 1200MHz |
| Channel | 8Ch | 8Ch | 4Ch |
| Output power | 0.5W | 0.5W/1W | 4W |
| Transmission range | Around 100~150M | Around 300~400M | Around 500~1000M |
| Power supply | 2,200mA/3.7VDC | 2,200mA/3.7VDC | 1.5A/12VDC外接 |
| Battery running time | 90 minutes (w/battery) | 50 minutes (w/battery) | Supply by power adapter |
| Dimension | 78x66x15 mm | 55x23x85 mm | 99x90x60 mm |
| Weight | Around 130g (w/battery) | Around 110g (w/battery) | Around550g (exclude battery) |

or

( Options:

- WRD-3 wrist-wear wireless A/V Receiver/Recorder

- JR-1208P wireless receiver

- Li rechargeable battery & charger (running time up to 3 hrs above)

- 10dB directional antenna for longer range transmitting

P.18

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.