# Text boxes

Raysun FS series

Various Fiber-scope Inspection Devices

Special surveillance Devices -16

FS-T1 Ultra-slim fiber-scope

FS-T3 Controllable fiber-scope

FS-T4 rigid fiber-scope

Diameter: Ø2.2mm

Tube length: 980mm

- Featuring hard stainless steel tube, can be forced into narrow places (such as gun barrel and machine...etc for inspection.

- Tube outer diameter:                                 FS-T4-I: Ø7mm；FS-T4-II: Ø5mm

- LED light source.

- FS-T4-II can co-work with side-viewing mirror.

- 2-way articulations control right/left turning of the lens, over 90 degree turning angle.

- Scaled polyurethane rubber covered tube, water, oil, weak-acid/alkali proof, tube is scaled to indicate the length of insert. Capable for checking of industrial devices, drainage system, aviation security, research & study...etc. and many other applications.

- Tube outer diameter: Ø6mm, total length: 1860mm.

- Comes with LED light source which is interchangeable according to the applications.

- Can co-work with C-mount CCD, 25mm camcorder & side-viewing mirror.

- Ultra-slim fiber-scope, tube outer dia. Is only Ø2.2mm

- Easy carry/operation, directly eye-viewing.

- Tube operation length: 980mm, total length: 1045mm

- Weight: 75g only.

- Can co-work with C-mount CCD & 25mm camcorder.

With LED light

Co-work with side-viewing mirror

FS-T3 Controllable fiber-scope

Two-way articulations

LED light

Tube scaled to indicate length/depth of insert

( Specifications:

| Type | Ultra-slim | Controllable | Rigid |
| --- | --- | --- | --- |
| Model | FS-T1 | FS-T3 | FS-T4-I | FS-T4-II |
| Optics system | FOV | 44° |
|  | Viewing direction | Straight | Straight /Side-viewing | Straight | Straight /Side-viewing |
|  | Lighting system | -- | Fiber-lead lighting system |
|  | Tube water-proof | √ | √ | √ |
| Front-end lens outer diameter | Φ4.0mm ±5% | Φ6mm±5% | Φ7.0mm±5% | Φ5.0mm±5% |
| Insert tube outer diameter | Φ2.2mm ±5% | Φ6mm±5% | Φ7.0mm±5% | Φ5.0mm±5% |
| Tube operation length | 980±20 mm | 1860±20 mm | 510±20 mm | 550mm |
| Full length | 1045±20 mm | 1860±20 mm | 600±20 mm | 650mm |
| Tube bending | Flexibly bending | Flexibly bending | -- |
| Front-end lens articulation control | -- | Mechanical control, right/left: 90º turning | -- |
| Power supply | -- | CR123A *1 | AA *1 |
| Weight (w/standard light) | 70g±5% | 415g±5% | 215g±5% | 145g±5% |
| Can co-work with CCD camera or camcorder | √ | √ | -- | √ |
| Can co-work with 90° side-viewing mirror | -- | √ | -- | √ |

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

P.24