# Text boxes

Raysun FS-E2

Wide FOV with invisible IR light Stretchable Video-scope

Special surveillance Devices-17-1

- High sensitivity / low lux CCD camera, integrated with IR illuminator that has an affective range of 3 meters. Allowing monitoring and recording under complete dark environment without exposure.

- Light weight and easy to operate. Ideal for industrial examination, security inspection, car chassis checking, and especially for police & military tactical purpose.

- Unique extendable design along with semi-rigid tube, provides exceptional reach and adjustable viewing angle.

- Multiple operation modes:

Mode A: Monitoring/recording only.

Mode B: Wireless transmitter + wrist-wear wireless A/V receiver/recorder.

Mode C: Monitoring/recording/transmitting + wrist-wear wireless receiver/recorder.

Extendable bar

(4 levels)

Bendable semi-rigid tube to manually adjust viewing directions

Optional 3 different setups for application

FS-E2

* 158° ultra wide FOV IR sensible camera (w/IR LED light)

* Φ20mmx75mm

* Bendable semi-rigid tube: Φ10mm x 20cm

* IR invisible light

* Effective illuminating range to approx. 3M

Co-works with wireless transmitter and WRD-3 wrist-wear wireless A/V receiver/recorder to easily & conveniently operation.

* Camera integrates with IR illuminator.

* Additional visible/ invisible LED light is available to enhance the lighting even further.

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.

( Specifications:

| Model | FS-E2 |
| --- | --- |
| Day/night mini color CCD camera | Lens | 2.1mm, FOV: 158° |
|  | Image sensor | 1∕4” SONY color CCD |
|  | Min. Luminance | 0.02 Lux |
|  | Camera dia. | Φ20×75mm |
|  | Electronic shutter | 1/60～1/100000 |
|  | Pixels | NTSC:768(H)×496(V) |
|  | Power supply | 123A Lithium Battery *2 |
|  | Resolution | 520TV Lines |
|  | Running Time | Around 240 minutes |
| Infrared LED | IR LED Light x 8 |
| Length before extension | Around 80 cm |
| Length after extension | Around 190 cm |
| Extend level | 4 |
| Weight | Within 650g (exclude battery) |

Optional visible/invisible auxiliary light

LED輔助光源

Ultra wide FOV to around 158°

Record/observation without dead zone

( Options:

- DVR-2 Plus digital recorder

- JT-1205C6 500mW wireless transmitter

- DVR-2 + wireless transmitter

- WRD-3 wrist-wear wireless A/V receiver/recorder

- Head-wear monitor (Ideal for monitoring under bright sunlight)

- JR-1208P wireless A/V receiver

- Additional IR LED light

- Additional LED light

IR sensible, extra low illumination to 0.02Lux

Color/B&W auto change to get clear image

P.25

本型錄內容說明、規格如有調整修訂，不另通知。