# Text boxes

Raysun FS-EVD-III

Electronic Video-scope Inspection Device

Special surveillance Devices -18-2

- FS-EVD-III is integrated with miniature camera, A/V transmitter, high resolution DVR & lighting system, which achieved more functions & much better performance than any other conventional fiber-scopes.

- Built-in high sensitive microphone to transmit voice from operator to the remote site associates or supervisor for monitoring synchronously.

- 4-way articulations for camera inspecting directions control; LED light source; tube external diameter: 6mm only.

- Can be easily operated by single hand.

- Polyurethane rubber covered tube for well protection with insert length/depth measurement indication.

- It’s ideal for industry, drainage system, aircraft, national defense, law enforcement, scientific research, …etc applications.

Photography/Recording/

Transmission

( Remote monitoring

( Image performance

RX

TX

(1). Transmit A/V signal to WRD-3 wrist-wear wireless A/V receiver/recorder

RX

Gun barrel checking (auxiliary light ON)

Under normal lighting environment (auxiliary light OFF)

(2). Transmit A/V signal to JR1208P wireless A/V receiver and output it to the connected monitor

(特色說明

( Specifications:

| Model | FS-EVD-III |
| --- | --- |
| Resolution | 480 TV LINE |
| Image sensor | Super Color VGA Sensor |
| Min. illumination | 2 Lux / F2.8, effective pixels: 720X525 |
| Electronic shutter | 1/60~1/62500 |
| Lens(FOV) | 0.96mm(F2.8)/60° |
| Auxiliary light | 4 LED lights |
| Tube outer dia. | Ø6mm |
| Articulation control | Up/down/left/right, 360∘ full direction control |
| Tube operation length | Around 180cm above |
| Wireless transmission | 1200MHZ/6 CH |
| Output power | 200mW(0.2W) |
| Transmission range | Around 100M |
| Battery running time | Around 70 minutes |
| Power | 3.6V/1800mA |
| Dimension (exclude sticking out part) | Around 300 x110x90 mm |
| Weight | Around 770g |
| Record resolution | 720 x480@18fps 640x480@30fps |
| Memory | SD HC card |
| Date/time | Y/M/D/H/M/S |
| Low power indication | yes |

( Standard package:

- FS-EVD-III main body

- 90∘side-viewing mirror

- Aluminum hard suitcase

Insert length/depth measurement indication

Ultra mini camera with light for checking into the darkness

P.28

Full direction control

>180°

360∘4-way turning

Articulation control

Additionally add

( Option:

- JR1208P wireless A/V receiver

- WRD-3 wrist-wear wireless A/V receiver/recorder

Lens end

Side viewing mirror

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.