# Text boxes

VISA-2

Hand-Held intelligent Metal Detector

Special surveillance Devices -19

P.30

- Features auto scan with high sensitivity.

- Effectively detect small hidden metals such as a pin, razor blades, knives…etc.

- 2 operation mode: Sound and Mute (Vibration).

- Intelligent LED lamp indicator, capable of showing metal capacity with lights-up level.

- Harmless to human body.

- Compact, light weight, easy to carry and operate.

Detection area (double sides)

Color light bar alarm indicates size of detected object

Battery condition indicator

Alarm selector

– Silent vibration or audio modes

Audio alarm Piezo

10 顆LED燈:

用於顯示金屬含量多寡

Belt carrying

Power switch (In=ON; Out=OFF)

Silent vibration alarm built into handle

( Specifications:

| Operation freq. | 95KHz |
| --- | --- |
| Audio freq. | 2KHz |
| Operation voltage | 6.8－10 volts |
| Power | 1 9V regular or Alkaline battery |
| Consumption current | 5mA |
| Intelligent detection system | Green/yellow/red 3-step total 10 indicators of metal capacity detection |
| Silent (vibration ) mode | While push down (VIB.) button, vibration will generate when metal is detected without audio alarm |
| Dimension | 315(L)x50(W)x29(H)mm |
| Weight | Around 280g |

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.