# Text boxes

Raysun DN-680III

Day/Night Long Distance Spot-Scope

Optics & Night Vision Devices - 20

P.31

Available for observing/recording/ transmitting at night-time

Optional Night Visions for night-time usage

Eyepiece is replaceable

Optics adapter for NV coupling

Ultra low light CCD camera

DVR

Standard Day-time Eyepiece

Red-dot Sight (target seeker):

Mount by picatinny rail for easy installation.

Wireless transmitter

- Refractive telescope, extra large objective lens (110mm) for more incoming light to result in higher image performance.

- 680mm optics focal length, capable of recognizing 302cm objects under darkness at a distance up to 500m while working with night vision goggles/monocular.

- Comes with an optics adapter for various CCD camera & NV integration, and 25, 30, 37mm adapters for various DV camcorders integration.

- Anti-corrosion coating with aluminum alloy housing, nitrogen gas filled, compact and endurable, light weight.

- Co-work with optional inner-projected Red-dot Sight (target seeker) for easier & faster target searching.

Co-work with NV and DV camcorder for night-time viewing/recording

Co-work with DV camcorder for day-time viewing/recording

( Options:

- 0.00002 lux day/ night camera

- DVR-2 gigital recorder

- Various transmitters /receivers

- Various NVs

( Standard package:

- 680mm Spot-scope main body

- Day-time eyepiece, include *25mm standard lens *2

- NV & CCD optics adapter

- Sunshade & lens cover

- 25、30、37mm Camcorder adapters

- Hard case & carry bag

( Specifications:

| Item | Description |
| --- | --- |
| Optics System | Refractive Telescope |
| Objective diameter | 110mm |
| Objective focal length | 680mm |
| Eyepiece | (1). Day-time eyepiece (2). Night-time eyepiece: Various Night Vision Goggle/Monocular |
| Focus adjustment | Mechanical |
| Field of view with day-time eyepiece | (1). Standard 25mm Lens: 1.85˚ (2). 7~21mm zoom Lens: 0.52~1.56˚ |
| Sunshade | ( |
| Waterproof | IP-x4 |
| Weight | < 3500g |

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.