# Text boxes

Raysun NVS-III

Hand-held Night Vision Monocular

Optics & Night Vision Devices - 23

Co-work with camcorder

Co-work with 10X lens

Co-work with CCD

Configurations

Coupling Adapter

10X zoom lens

- Built-in HyperGen or Gen 3 Image Intensifier Tube (IIT), eXTreme grade (High FOM, equivalent to Gen. 3 US and XD-4, better than US export restrained standard of FOM).

- Can be integrated with our DN-680III, camera, DV Camcorder & CCD camera.

- Built-in 5mW infrared illuminator for illuminating in the totally dark places.

- Clear image, high Luminance gains, compact, light weight, easy for carry & operation.

- Objective lens can be changed by various CCD lens or camera zoom lens via adapter coupling.

Eye shield

Standard lens

Handle

( Standard package:

- NVS-III main body

- 25mm standard lens

- Hand/neck strap

- Handle

- 25/30/37mm Camera/Camcorder Adapter

- 37→52mm Adapter

- Carrying bag

CCD adapter

Tripod

( Specifications:

| Objective lens | Standard 25 mm lens |
| --- | --- |
| Objective F number | F 1.2 |
| Field of view | 40˚ |
| Objective lens mount | CCD, C-mount adapter |
| Eyepiece diameter | 25mm |
| Dioptric correction | ±5 |
| Image Intensifier Tube (IIT) | Grade | HyperGen | Gen 3 |
|  | Luminance gains, FL/FC, min. | 40,000 fl/fc at 10-6 fcd |
|  | Sensitivity, µA/lm | 600-750 | 1200 above |
|  | Resolution, Lp/mm | 57-64 |
|  | S/N ratio | 20-23 | 20-24 |
|  | MTBF, hours | 10,000 |
| Power switch | 3-step: OFF/ON/IR |
| Dimensions (just main body of monocular), mm | 85×50×70mm |
| Weight (just main body of monocular), g | 380g |
| Power / Running time | DC 3V Lithium battery /45 hours |

Standard package

( Options:

- 4X lens

- 10X zoom lens, 16~160mm

- DN-680III spot-scope

- Camera/Camcorder Adapter

- CCD camera adapter

P.34

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.