# Text boxes

Raysun NVS-7

Multi-purposed Night Vision Goggles

Optics & Night Vision Devices

2. Helmet-wear (1X lens)

1. Head-wear (1x lens)

- Work with a 20X zoom lens

- C-work with our 680mm Spot-Scope for long distance observation

3. Add a 4X lens

- Built-in Gen 2+ Image Intensifier Tube (IIT),   with high FOM above 1260.

- Integrated power supply, provides Automatic Brightness Control (ABC) and Bright Source Protection (BSP) to guard against exposure to over brightness (Automatically shut down to protect IIT).

- Built-in 5mW infrared illuminator to enhance the  illumination under low light condition.

- Various optional C-mount objective lens (4X, 20x or others) can be used for long distance monitoring.

- Compact, endurable construction, light weight, waterproof and easy operation.

( Specifications:

| Model | NVS 7-2/XT |
| --- | --- |
| Image Intensifier Tube (IIT) | Image Intensifier Tube | 18 mm HyperGen |
|  | Grade | XT |
|  | Photocathode operating diameter, mm | 18 |
|  | Photocathode type | S-25 |
|  | Resolution, min, Lp/mm | 57-64 |
|  | Photocathode sensitivity, µA/lm | 600-750 |
|  | Luminous Gain, fL/fc, min | 40,000 fl/fc at 10-6 fcd |
|  | Image magnification | 1 |
|  | Dark background brightness, max. cd/m² | 1.5x10-3 |
|  | Signal-to-noise ratio, min. | 20-23 |
|  | Current consumption, max, mA | 16 |
|  | Mean time before failure, hours | 10,000 |
|  | Keep time, years | 15 |
| Magnification | 1x (can add 4x or 5X lens directly, option) |
| Field of view | 40° |
| Objective focal length, mm | 25 ~ ∞ |
| Objective F number | 1.2 |
| Eye relief, mm | 25 |
| Interpupillary distance, mm | 57-73 |
| Focus range, m | 0.25 |
| Dioptric correction | ±5 |
| Power supply | Standard AA batteries *2 |
| Battery life, hours | 80 (I/R off) above 40 (I/R on) above |
| Low battery indicator | V |
| I/R ON indicator | V |
| Dimensions (include 1X lens), mm | Approx. 183x132x58 |
| Weight (include 1X lens), g | 550 |

( Options:

- 4x lens

- 20x zoom lens (10~200mm, F1.9)

- 680mm Spot-Scope

- Helmet mount

( Standard package:

- Main body of NVS-7

- Standard 25mm lens(1x) Head gear

- Carry bag (with operation manual)

We reserve the right to vary, modify or improve any specification and/or design at any time without prior notice.