d

‘1

# Text boxes

Multifunctional Paintball Rifle

RAYSUN M4

Short barrel

|  | 0.68” Pepper ball |  | Fin stabilized pepper ball |
| --- | --- | --- | --- |
| Rubber ball | Fin stabilized rubber ball |
| Training ball | Fin stabilized training ball |
| Paintball |  |
| Blast ball |  |

Long barrel

Feature:

- M4 is a reliable milsim paintball gun allowing for feeding both regular caliber 0.68” paintballs and fin stabilized balls to help make an accurate shot at a long distance.

- Provide various kinds of balls to meet different purpose.

- The modularized design avoids the hassle of defective trouble.

- The only type in the market to include long barrel and short barrel, both can be interchanged for different mission, short barrel can be used as a sniper, while long barrel can have a effective range up to 40m if select fin stabilized balls.

- Permit to install disposable 88g gas bottle (“clap” to break gas bottle for immediate use) or refillable 5OZ gas tank in the buttstock; the gas refill bottle can be removed for reuse.

- Allow to adjust the front sight and hindsight depends on the barrel length.

- Quick-release & install design.

- Easy to carry and maintain.

- t.

Note: Do not use the fragile type of balls to prevent the device from being stained by the ball powder if get broken on impact.

Part name:

Specification:

Can be replaced as long barrel

| Caliber | 0.68” | Magazine capacity | 16 balls |
| --- | --- | --- | --- |
| Velocity | 300~450 fps depends on balls and barrel length | Shooting mode | Semi-shooting |
| Max range | 50m | Propellant | 88g Co2 gas bottle or gas refill tank |
| Dimension/ weight | 64 x 26 x 7(cm) / 2220g (long barrel) 41.5 x 26 x 7(cm) / 1830g (short barrel) |
| Material | Metal housing and barrel, plastic parts |

Lever

Safe/arm switch

Front sight

Hindsight

Gas bottle

Short barrel

Butt

Trigger

Gas refill adapter designed for clap type of gas bottle

Velocity adjustment

Magazine (16 balls in capacity)

Standard package:

88g gas bottle & buttstock

8.

9.

7.

10.

11.

12.

6.

1.M4 main unit

2.butt/short barrel

3.Long barrel

4.88g gas bottle

(not included)

5.Magazine

6.Nylon strap

7.Pepper ball

8.Fin stabilized training ball

9.Fin stabilized

rubber ball

10.Paint ball

11.Rubber ball

12.Training ball

13.Carry bag

14.Tool

5.

Replaced as 5oz gas refill tank & buttstock

Do not use in public, the user should take the responsibility for remodeling or illegal use of the device if any lawsuit arises.

13.

14.

4.

3.

1.

2.

Attach to laser aimer

Attach to illuminator

Parachute Illuminator

Waterproof Smoke

10M Net Gun

110M Line Thrower

60M Life Buoy

Colored Smoke